## Slide 1: “Fingerprint” extraction from the Stanford DAS recordings
Siyuan Yuan
March 23, 2018
2018 SEP Annual meeting
SEP172, page 15-26

## Slide 2: Overview
Background and motivation
Inverse problem set up
  Model space and data space
  Forward and adjoint
  Inversion
Synthetic analysis
  Impulsive plane wave
  Reverberant plane wave
Field data application
  Foothill earthquake

## Slide 3: What is DAS?
It is a laser-based sensor system measuring changes in a fiber-optic cable.
Advantages:
Low cost per sensor; dense sensor distribution

## Slide 4: Thousands of Earthquakes recorded
The Stanford DAS array started continuously
recording ground motion since Sep., 2016
Notes: Since DAS array installed, we have thousands of quake occurred around the bay area

## Slide 5: Stanford DAS recordings are extracted based on the USGS online database
Yuan et al., SEP-170
Metadata
preprocessing
USGS online database
Event data
Event data (raw)
Data recorded by DAS

## Slide 6: Catalogue that can be continuously updated set up
Yuan et al., SEP-170
Data recorded by DAS
Metadata
preprocessing
USGS online database
Event data (raw)
Event data
SEGY
& SEP3D
save
recorded
Event SQL
database

## Slide 7
One example of DAS recordings
Magnitude: 3.3
Distance: 32.8 km
09/15/2017 01:17:47 UTC time
N
Foothill earthquake
DAS
epicenter
P
S
Notes: In the east foothill area

## Slide 8
Can DAS recordings have “Fingerprints”?
Represent the major waveform characteristics
Filter out noise
Small size
save space and computational cost
Foothill earthquake
P
S
Notes: By representing major waveform: ignore the noise
Small size: save space and computational cost

## Slide 9: A few observations
Foothill earthquake
Anthropogenic noise is local with
low velocities.
Random noise is incoherent.
Earthquake data have fast
velocities, are coherent through
most of the channels
(dominant plane waves with
relatively fast velocities.)
P
S

## Slide 10: “Fingerprints” represent dominant plane-wave components
“Fingerprint”
What are the dominant
plane waves?
Propagation directions?
Apparent velocities?
Compositions of compressional
and shear waves?
Foothill earthquake
Feature
extraction
P
S

## Slide 11: “Fingerprints” represent dominant plane-wave components
Earthquake
recovery
What are the dominant
plane waves?
Propagation directions?
Apparent velocities?
Compositions of compressional
and shear waves?
Foothill earthquake
Feature
extraction
“Fingerprint”

## Slide 12: Big picture
~ 3,000 DAS recordings catalogued!
Yuan et al., SEP-170

## Slide 13: Big picture
“Fingerprint” Library
~ 3,000 DAS recordings catalogued!
Yuan et al., SEP-170
Low noise level
Small data size

## Slide 14: Big picture
~ 3,000 DAS recordings catalogued!
Yuan et al., SEP-170
Statistical learning
for earthquake
detection and
location!
https://www.cio.com/article/3235508/cio-role/why-cios-need-a-chief-artificial-intelligence-officer.html
“Fingerprint” Library

## Slide 15: Our focus
~ 3,000 DAS recordings catalogued!
Yuan et al., SEP-170
https://www.cio.com/article/3235508/cio-role/why-cios-need-a-chief-artificial-intelligence-officer.html
“Fingerprint” Library
Statistical learning
for earthquake
detection and
location!

## Slide 16: Overview
Background and motivation
Inverse problem set up
  Model
  Forward operator
  Inversion
Synthetic analysis
  Impulsive plane wave
  Reverberant plane wave
Field data application
  Foothill earthquake

## Slide 17: “Fingerprint” extraction: an inverse problem
What are the dominant
plane waves?
Propagation directions?
Apparent velocities?
Compositions of compressional
and shear waves?
Foothill Earthquake Data
Model
Data
inversion
forward
Plane wave
superposition
Plane wave
extraction

## Slide 18: Model: m (ϕ, c)
E
N
ϕ
Wave front
c: horizontal slowness
0 ~ 0.002 s/m <=> 500 ~ m/s
Chosen based on prior knowledge
Φ: propagation direction
0 ~ 2
c

## Slide 19: Compressional and shear waves have different fiber responses
Shear wave
Compressional wave
Polarity flipped at the
interceptions of the
orthogonal fibers
No polarity flipped at the
interceptions of the
orthogonal fibers
Notes: Introduce Quary blast data: Epicenter 13 km away; Shallow
Emphasize shear wave

## Slide 20: Incorporate wave type into the model space
E
N
ϕ
Wave front
c: horizontal slowness
0 ~ 0.002 s/m <=> 500 ~ m/s
Chosen based on prior knowledge
Φ: propagation direction
0 ~ 2
w: wave type
compressional or shear wave
c
m (ϕ, c, w=0)
m (ϕ, c, w=1)
Compressional
wave
Shear wave

## Slide 21: Fiber responses for compressional and shear waves
Fiber 1
Fiber 2
Ratio
Compressional
wave
Shear
wave
Martin et al., SEP-168
fiber 1
fiber 2
Wave propagation direction

## Slide 22: Forward Operator: ensemble of plane-wave impulse responses
mk (ϕk, ck, wk), t0
mk
Mk
ml
Ml
=
d
F
m
d
=

## Slide 23: Solve for the model (“fingerprint”)
adjoint (beamforming)
inverse with L-2 norm
inverse with L-1 norm
make the model sparse
find the most relevant plane waves
Notes: We like few model points: L1-norm can potentially do that

## Slide 24: Overview
Background and motivation
Inverse problem set up
  Model
  Forward operator
  Inversion
Synthetic analysis
  Impulsive plane wave
  Reverberant plane wave
Field data application
  Foothill earthquake

## Slide 25: Simplified geometry

## Slide 26: Synthetic model (ground truth)
b1
b2
b3
r1
r2
r3
EQ
compressional
wave
shear wave
Notes: Loop through different t0 to find wave
with different phases

## Slide 27: Synthetic data: forward modeling
b1
b2
b3
r1
r2
r3
EQ
r1
r2
r3
b3
b1
b2
Notes: Loop through different t0 to find wave
with different phases

## Slide 28: Synthetic data: forward modeling
b1
b2
b3
r1
r2
r3
EQ
r1
r2
r3
b3
b1
b2
compressional wave
shear wave
Notes: Loop through different t0 to find wave
with different phases

## Slide 29: One challenge: compressional wave is interfered by the shear wave
r1
r2
r3
b3
b1
b2
b1
b2
b3
r1
r2
r3
EQ
Notes: Loop through different t0 to find wave
with different phases

## Slide 30: Adjoint: “Fingerprints” with spread-out energy
compressional wave “fingerprint”
shear wave “fingerprint”

## Slide 31: Adjoint: “Fingerprints” with spread-out energy
compressional wave ground truth
shear wave ground truth

## Slide 32: L-2 norm inversion “Fingerprints”: better but not great
compressional wave “fingerprint”
shear wave “fingerprint”
Notes: Loop through different t0 to find wave
with different phases

## Slide 33: L-2 norm inversion “Fingerprints”: better but not great
compressional wave ground truth
shear wave ground truth
Notes: Loop through different t0 to find wave
with different phases

## Slide 34
L-1 norm inversion “Fingerprints”: highly sparse and focused
compressional wave “fingerprint”
shear wave “fingerprint”
# of nonzeros: 2
Notes: Loop through different t0 to find wave
with different phases

## Slide 35
L-1 norm inversion “Fingerprints”: highly sparse and focused
compressional wave ground truth
shear wave ground truth
# of nonzeros: 2
Notes: Loop through different t0 to find wave
with different phases

## Slide 36
L-1 norm inversion “Fingerprints”: waveform well recovered
Recovered waveform
Notes: Loop through different t0 to find wave
with different phases

## Slide 37
L-1 norm inversion “Fingerprints”: waveform well recovered
Synthetic data
Notes: Loop through different t0 to find wave
with different phases

## Slide 38
Waveform is compressed to two “Fingerprint” points !
Synthetic data
“fingerprints”
Notes: Loop through different t0 to find wave
with different phases

## Slide 39: We have seen reverberation in field data
Foothill earthquake data
Notes: Loop through different t0 to find wave
with different phases

## Slide 40: Switch from synthetic impulsive waves to reverberating waves
r1
r2
r3
b3
b1
b2
b1
b2
b3
r1
r2
r3
EQ
Notes: Loop through different t0 to find wave
with different phases

## Slide 41: Switch from synthetic impulsive waves to reverberating waves
r1
r2
r3
b3
b1
b2
b1
b2
b3
r1
r2
r3
EQ
Notes: Loop through different t0 to find wave
with different phases

## Slide 42: Synthetic model for reverberating waves: periodic function of t0
compressional wave ground truth
shear wave ground truth
Notes: Loop through different t0 to find wave
with different phases

## Slide 43: Adjoint “Fingerprints”
Compressional waves: NOT recovered!
Shear waves: recovered with spread-out energy.

## Slide 44: Inversion with L2 regularization “Fingerprints”
Compressional waves: obvious artifacts
Shear waves: fairly well recovered.
Notes: Loop through different t0 to find wave
with different phases

## Slide 45
Inversion with L1 regularization:
Plane waves are well recovered
Notes: Loop through different t0 to find wave
with different phases

## Slide 46
Waveform is compressed to sparse “Fingerprint” points
Synthetic data
“fingerprints”
Notes: Loop through different t0 to find wave
with different phases

## Slide 47: Conclusions of the synthetic tests
Adjoint:
a rough estimation and it suffers from crosstalk artifacts.
L2 norm inverse:
better compared to the adjoint method.
L1 norm inverse:
highly focused results with no obvious artifacts.

## Slide 48: Overview
Background and motivation
Inverse problem set up
  Model
  Forward operator
  Inversion
Synthetic analysis
  Impulsive plane wave
  Reverberant plane wave
Field data application
  Foothill earthquake
Notes: Loop through different t0 to find wave with different phases
Mention 2D model space

## Slide 49
Foothill earthquake
Magnitude: 3.3
Distance: 32.8 km
09/15/2017 01:17:47 UTC time
N
Foothill earthquake
P
S
Notes: Loop through different t0 to find wave
with different phases

## Slide 50
Foothill earthquake
Foothill earthquake
P
S
Notes: Loop through different t0 to find wave
with different phases

## Slide 51
Foothill earthquake
r1
r2
r3
b1
b2
b3
Foothill earthquake
P
S
r1
r2
r3
b1
b1
b2
b3
Notes: Loop through different t0 to find wave
with different phases

## Slide 52
r1
r2
Foothill earthquake
r3
b1
b2
b3
Extract data for test
Extracted data
P
S
P
S
r1
r2
r3
b1
b2
b3
b1
Notes: Loop through different t0 to find wave
with different phases

## Slide 53
L1 inverse extracts the most sparse “Fingerprints”
adjoint
L2 inverse
L1 inverse
2,896 (1.0%)
270,954 (94.1%)
270,954 (94.1%)
compressional
wave
shear wave
# of non-zeros
Notes: Loop through different t0 to find wave
with different phases

## Slide 54
L1 inverse recovered the major waveforms
adjoint
L2 inverse
L1 inverse
Notes: Loop through different t0 to find wave
with different phases

## Slide 55
L1 inverse recovered the major waveforms
Data recovered by L2 inverse
Data recovered by L1 inverse
Notes: Loop through different t0 to find wave
with different phases

## Slide 56
L1 inverse recovered the major waveforms
Field data
Notes: Loop through different t0 to find wave
with different phases

## Slide 57
L1 inverse recovered the major waveforms
L2 inverse difference
L1 inverse difference
Notes: Loop through different t0 to find wave
with different phases

## Slide 58
Field data are compressed to sparse “Fingerprints”
“fingerprints”
Field data
2,896 non-zeros
14,730 non-zeros
Notes: Loop through different t0 to find wave
with different phases

## Slide 59: Conclusions
L1 norm inverse can give us highly sparse results and recover the earthquake data ignoring the noise.
L1 norm inverse can be potentially used to extract “fingerprints” from
DAS recordings to set up earthquake detection and location
algorithms.
Notes: Loop through different t0 to find wave
with different phases

## Slide 60: Aknowledgements
Stanford Center for Induced and Triggered Seismicity for financial support
OptaSense for DAS equipment available.
Stanford Center for Computational Earth and Environmental Sciences for computing resources.
Stanford IT and SEEES IT for supporting the installation.
Our colleagues for help, especially Bob Clapp, Eileen R. Martin, Yinbin Ma.
Notes: Loop through different t0 to find wave
with different phases

## Slide 61: Questions?
Notes: Loop through different t0 to find wave
with different phases