## Slide 1: Toward time-lapse study of anisotropic parameters over the Genesis field
Yinbin Ma
05/22/2018
Stanford Exploration Project
Ma et al., SEP 172, 2018

## Slide 2
Motivation
Is there a measurable 4D anisotropic effect?
M. Maharramov, Ph.D. Thesis, SEP-162, 2016
Time-lapse velocity change

## Slide 3
Outline
Data re-processing
Time-lapse RTM study
Sensitivity analysis for anisotropic parameters

## Slide 4
Outline
Data re-processing
VTI model
Time-lapse RTM study
Possibility of estimating anisotropic parameters with 4D FWI
Purpose: register RTM images from multiple datasets for better estimation of 4D effect

## Slide 5
Baseline survey, 1990
Magesan, et al., 2005
Acquisition geometry for GENESIS dataset

## Slide 6
Baseline survey, 1990
Monitor survey, 2002
Magesan, et al., 2005
Acquisition geometry for GENESIS dataset

## Slide 7
Baseline survey, 1990
Monitor survey, 2002
Magesan, et al., 2005
Acquisition geometry for GENESIS dataset

## Slide 8
Baseline survey, 1990
Monitor survey, 2002
Magesan, et al., 2005
Acquisition geometry for GENESIS dataset
2D line used in this presentation
Pros: no acquisition gap
Cons: less 4D effect

## Slide 9
Example of midpoint gather before data processing
Co-processed baseline and monitor data

## Slide 10
Example of midpoint gather before data processing
Co-processed baseline and monitor data
Processed separately

## Slide 11
Example of midpoint gather before data processing
Different range of offset

## Slide 12
Example of midpoint gather before data processing
Different amplitude correction

## Slide 13
Example of midpoint gather before data processing
Different signal to noise ratio

## Slide 14
Difference between two monitor datasets: ADCIG

## Slide 15
Effect from actual production vs effect from processing
Effect of time-lapse change
Red circle: location of reservoir, time-lapse change expected
Green arrow: locations where RTM images should register

## Slide 16
Effect from actual production vs effect from processing
Effect of time-lapse change
Effect of processing
Red circle: location of reservoir, time-lapse change expected
Green arrow: locations where RTM images should register

## Slide 17
Understanding the header with semblance scan
Conventional semblance scan over velocity (NMO)
Travel time fixed
Zero offset travel time fixed
Offset fixed
Scan over stacking velocity

## Slide 18
Understanding the header with semblance scan
Our approach to understand the header information
Travel time fixed
Zero offset travel time fixed
Scan over offset
Fixed velocity for water bottom reflection

## Slide 19
Understanding the header with semblance scan
Our approach to understand the header information
Scan over time axis
Zero offset travel time fixed
Offset fixed
Fixed velocity for water bottom reflection

## Slide 20
New interpretation of the header information
Our initial interpretation of the time shift
new interpretation of the time shift
12 ms shift is a lot to us, because the time-lapse change is about 10 meters

## Slide 21
New interpretation of the header information

## Slide 22
Our “optimal” re-processing workflow
shift midpoint location;
align sources and receivers with the boat sailing direction;
shift origin of offset axis from 400 ft to 360 ft;
shift zero time by 6 ms;
apply spherical divergence correction to match the baseline data;
apply NMO correction to flatten the CMP gather;
interpolate along offset axis;
apply inverse NMO correction to recover kinematics;
sort to shot and receiver gathers to enhance illumination.

## Slide 23
Example of midpoint gather before data re-processing

## Slide 24
Common shot gathers after data re-processing

## Slide 25
Common shot gathers after data re-processing

## Slide 26
A brief summary of our data-reprocessing

## Slide 27
A brief summary of our data-reprocessing
Initial interpretation

## Slide 28
A brief summary of our data-reprocessing
Initial interpretation
Updated interpretation

## Slide 29
A brief summary of our data-reprocessing
Initial interpretation

## Slide 30
A brief summary of our data-reprocessing
Initial interpretation
Updated interpretation

## Slide 31
Outline
Data re-processing
Time-lapse RTM study
Sensitivity analysis for anisotropic parameters

## Slide 32
3D VTI model: vertical velocity
Ma et al., SEP 168, 2017

## Slide 33
3D VTI model: η parameter
Ma et al., SEP 168, 2017

## Slide 34
RTM image with 3-35 Hz data
Anisotropic migration of baseline
Stretch mute will remove low freq at shallow area

## Slide 35
RTM image with 3-35 Hz data
Anisotropic migration of monitor-1
Stretch mute will remove low freq at shallow area

## Slide 36
RTM image with 3-35 Hz data
Anisotropic migration of monitor-2
Stretch mute will remove low freq at shallow area

## Slide 37: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of baseline

## Slide 38: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of monitor-1

## Slide 39: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of monitor-2

## Slide 40: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of baseline

## Slide 41: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of baseline

## Slide 42: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of monitor-1

## Slide 43: Analysis of depth-shifts in migrated images stacked images
Near offset see the velocity decreasing area, not far offset
V-

## Slide 44: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of monitor-1

## Slide 45: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of monitor-2

## Slide 46: Analysis of depth-shifts in migrated images stacked images
Anisotropic migration of baseline

## Slide 47
Outline
Data re-processing
Time-lapse RTM study
Sensitivity analysis for anisotropic parameters

## Slide 48
Anisotropic migration of monitor-2
With correction anisotropic parameters

## Slide 49
Anisotropic migration of monitor-2
With increased anisotropic parameters (3x eta)

## Slide 50
Anisotropic migration of monitor-2
With increased anisotropic parameters (10x eta)

## Slide 51
Anisotropic migration of monitor-2
With correction anisotropic parameters

## Slide 52
Anisotropic migration of monitor-2
With increased anisotropic parameters (20x eta)

## Slide 53
Conclusions
RTM images register after data re-processing
Time-lapse RTM study confirmed detectable 4D effect in seismic data
Far offset data sensitive to anisotropic parameters

## Slide 54
Thank you and questions?
We would like to thanks Chevron, ExxonMobil and BHP for giving us the Genesis dataset.