## Slide 1: Time-lapse FWI with shaping regularization: toward integrated reservoir monitoring
Yinbin Ma
05/22/2018
Stanford Exploration Project

## Slide 2
Motivation:
Better results when combining different types of data
Inversion with seismic data alone
Y. Ma et al., SEP 158, 2015

## Slide 3
Motivation:
Better results when combining different types of data
Inversion with seismic data alone
Inversion with extra geological dip info
Y. Ma et al., SEP 158, 2015

## Slide 4
Outline
Challenges for integrated reservoir monitoring
Regularization to combine different types of data
Numerical Examples on time-lapse FWI

## Slide 5
Outline
Challenges for integrated reservoir monitoring
Regularization to combine different types of data
Numerical Examples on time-lapse FWI

## Slide 6
Challenges from Genesis field
How to combine different types of data for integrated reservoir monitoring?
M. Maharramov, 2016
velocity change from seismic data

## Slide 7
Challenges from Genesis field
How to combine different types of data for integrated reservoir monitoring?
M. Maharramov, 2016
J. Rkckett et al., 2007
velocity change from seismic data
Geomechanical modeling

## Slide 8
Challenges from Genesis field
How to combine different types of data for integrated reservoir monitoring?
M. Maharramov, 2016
J. Rkckett et al., 2007
N. Hodgson et al., 2007
velocity change from seismic data
Geomechanical modeling
Pressure change from reservoir simulation

## Slide 9
Different types of data have different coverage and resolution
D. Johnston, Practical Applications of Time-lapse Seismic Data, 2013

## Slide 10
Undetermined parameters between different types of data
J. Rkckett et al., 2007
Seismic
geomechanics

## Slide 11
Undetermined parameters between different types of data
J. Rkckett et al., 2007
Seismic
geomechanics

## Slide 12
Outline
Challenges for integrated reservoir monitoring
Regularization to combine different types of data
Numerical Examples on time-lapse FWI

## Slide 13: FWI objective function
We use FWI objective defined on data misfit :
The subsurface model is estimated by:
m: subsurface model, velocity, anisotropic parameters, elastic parameters, etc
u: synthetic data
d: observed data

## Slide 14: Time-lapse FWI objective function
We use joint inversion approach:
Subscript: b for baseline, m for monitor
W: weight function
R: regularization operator
mprior: prior time-lapse change

## Slide 15: Time-lapse FWI objective function
We use joint inversion approach:
Subscript: b for baseline, m for monitor
W: weight function
R: regularization operator
mprior: prior time-lapse change
Data fitting for baseline survey

## Slide 16: Time-lapse FWI objective function
We use joint inversion approach:
Subscript: b for baseline, m for monitor
W: weight function
R: regularization operator
mprior: prior time-lapse change
Data fitting for monitor survey

## Slide 17: Time-lapse FWI objective function
Subscript: b for baseline, m for monitor
W: weight function
R: regularization operator
mprior: prior time-lapse change
Regularization on time-lapse change
We use joint inversion approach:

## Slide 18: Time-lapse FWI objective function
Subscript: b for baseline, m for monitor
W: weight function
R: regularization operator
mprior: prior time-lapse change
Regularization on time-lapse change
We use joint inversion approach:
How do we build the prior model?

## Slide 19: Prior model building
We can build prior model based on reservoir simulation:
D. Johnston, Practical Applications of Time-lapse Seismic Data, 2013

## Slide 20: Prior model building
We can build prior model based on reservoir simulation:
We can also build prior model based on geomechanics:
D. Johnston, Practical Applications of Time-lapse Seismic Data, 2013

## Slide 21: Prior model building
We can build prior model based on reservoir simulation:
We can also build prior model based on geomechanics:
D. Johnston, Practical Applications of Time-lapse Seismic Data, 2013
The challenge is that we do not know vinf, A, R

## Slide 22: Regularization without accurate prior
We assume 4D seismic property is linearly related to prior:
pprior: prior time-lapse change, vertical strain, stress, etc

## Slide 23
We assume 4D seismic property is linearly related to prior:
Measure of similarity between m and pprior:
pprior: prior time-lapse change, vertical strain, stress, etc
Regularization without accurate prior

## Slide 24: Proposed 4D FWI objective function
We use the following objective function:

## Slide 25: Proposed 4D FWI objective function
We use the following objective function:
Data fitting
Regularization

## Slide 26: Understand the objective function with 1D model
1D transmission problem:
two layers, each with 1 km, v1=1.5 km/s, v2=2.5 km/s
Data generated Ricker wavelet with peak freq 10 Hz
Data fitting term

## Slide 27: Understand the objective function with 1D model
1D transmission problem:
two layers, each with 1 km, v1=1.5 km/s, v2=2.5 km/s
Data generated Ricker wavelet with peak freq 10 Hz
ratio of v1/v2 used as prior for the regularization term
Data fitting term
Regularization term

## Slide 28: Understand the objective function with 1D model
1D transmission problem:
two layers, each with 1 km, v1=1.5 km/s, v2=2.5 km/s
Data generated Ricker wavelet with peak freq 10 Hz
ratio of v1/v2 used as prior for the regularization term
Total objective function

## Slide 29: Understand the objective function with 1D model
1D transmission problem:
two layers, each with 1 km, v1=1.5 km/s, v2=2.5 km/s
Data generated Ricker wavelet with peak freq 10 Hz
ratio of v1/v2 used as prior for the regularization term
Total objective function
Multiple local minimum

## Slide 30
Outline
Challenges for integrated reservoir monitoring
Shaping regularization to combine different types of data
Numerical Examples on time-lapse FWI

## Slide 31: True baseline model

## Slide 32: Starting model

## Slide 33: True time-lapse change

## Slide 34: True time-lapse change
Overburden dilation
Fluid substitution

## Slide 35: Inversion with no regularization

## Slide 36: Inversion with regularization

## Slide 37: Inversion with regularization

## Slide 38: Inversion with strong regularization
Wrong because it is beyond the resolution of seismic data

## Slide 39: Baseline data residual with noise

## Slide 40: Inversion without regularization

## Slide 41: Inversion with regularization

## Slide 42: Inversion with regularization

## Slide 43: Inversion with strong regularization

## Slide 44
Conclusion and future work
We explored one possible method for integrated reservoir monitoring
Test on field data where both seismic modeling and geomechanical modeling are available

## Slide 45
Thank you and questions?