## Slide 1: Full waveform inversion by model extension using a model-space multi-scale approach (FWIME)
Guillaume Barnier* and Ettore Biondi*
SEP 176, pp. 11-30
May 14th, 2019

## Slide 2: FWIME in a nutshell
The product
  Robust acoustic velocity-model building algorithm
The features
  Inaccurate initial models
  No need for low-frequency + long-offset data
  User-friendly
  Deployable to 3D field data
The results
  Diving waves (sep172)
  Reflection data

## Slide 3: FWIME in a nutshell
The product
  Robust acoustic velocity model building algorithm
The features
  Inaccurate initial models
  No need for low-frequency + long-offset data
  User-friendly
  Deployable to 3D field data
The results
  Diving waves (sep172)
  Reflection data

## Slide 4
Initial model

## Slide 5
Conventional FWI
Full data (reflections + refractions)
Data-space multi-scale (4-15 Hz)

## Slide 6
FWIME
Reflections only (6km maximum offset)
Model-space multi-scale (4-15 Hz)

## Slide 7
FWIME + FWI

## Slide 8
True model

## Slide 9
FWIME + FWI

## Slide 10
Conventional FWI

## Slide 11: Outline
Step-by-step dissection of FWIME
Inversion of reflection data
Making it feasible in 3D
Conclusions and opportunities

## Slide 12: Dissection of FWIME: How does it work?

## Slide 13: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
Gradient

## Slide 14: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
Gradient

## Slide 15: Conventional FWI
Predicted data
Observed data
Current model estimate

## Slide 16: FWIME objective function
: Data correcting term

## Slide 17: FWIME objective function
: Data correcting term
: Enhances energy of data-correcting term
: Trade-off parameter

## Slide 18: FWIME objective function
“Reduce the contribution
of the correcting term
over iterations”
“Make sure
match observed data”

## Slide 19: FWIME objective function
Data-fitting term
Regularization term
Notes: - Explain that if f~dobs, and g->0, then we found the same solution as fwi. Assuming that the solution is unique, this implies that we converged to the optimal solution
- In other word, the two formulations (FWI and FWIME) have the same global minimum
- Explain why our formulation has better chances of being more convex

## Slide 20: Sampling the objective function
x
Frequency: 2-35 Hz
Grid size: 10 m x 10 m
Source every 50 m
Receiver every 10 m
z
1 km
1 km

## Slide 21: Sampling the objective function
FWI

## Slide 22: Sampling the objective function

## Slide 23: Sampling the objective function
Regularization term
Data-fitting term
Total

## Slide 24: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
Gradient

## Slide 25: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
Gradient

## Slide 26: Data-fitting term
Goal of correcting term
Conventional Born modeling
Extended Born modeling
Notes: is your current velocity model guess!!!!!
𝑚_𝑖 is your current velocity model guess!!!!!

## Slide 27: Goal of correcting term

## Slide 28: Goal of correcting term

## Slide 29: Goal of correcting term
“Match all the events that your physical modeling was not able to match”
FWI data-residuals

## Slide 30: Numerical example – Velocity model
Interface
Interface
True velocity model
1D velocity profiles

## Slide 31: Numerical example - Data

## Slide 32: Conventional Born modeling

## Slide 33: Conventional Born modeling
: Born modeling operator
: Image (perturbation)
Born modeling operator
Image

## Slide 34: Conventional Born modeling – Dimensional analysis
x
z
receivers
time
shots
MODELING

## Slide 35: Conventional Born modeling – Dimensional analysis
x
z
receivers
time
shots
MIGRATION

## Slide 36: Conventional Born modeling

## Slide 37: Conventional Born modeling
Can we find that satisfies
this condition?

## Slide 38: Conventional Born modeling
2
2

## Slide 39: Conventional Born modeling
FWI data-residuals

## Slide 40: Conventional Born modeling

## Slide 41: Conventional Born modeling – Iteration #1

## Slide 42: Conventional Born modeling – Iteration #20

## Slide 43: Conventional Born modeling – Iteration #200

## Slide 44: Convergence curves
Conventional

## Slide 45: Extended Born modeling
: Extended Born modeling operator
: Extended image (perturbation)
Extended Born modeling operator
Extended image

## Slide 46: Extended Born modeling – Dimensional analysis
EXTENDED AXIS
x
z
receivers
time
shots
EXTENDED
MODELING

## Slide 47: Extended Born modeling – Dimensional analysis
EXTENDED AXIS
x
z
receivers
time
shots
EXTENDED
MIGRATION

## Slide 48: Extended Born modeling
FWI data-residuals

## Slide 49: Extended Born modeling

## Slide 50: Extended Born modeling – Iteration #1

## Slide 51: Extended Born modeling – Iteration #20

## Slide 52: Extended Born modeling – Iteration #200

## Slide 53: Convergence curves
Conventional

## Slide 54: Convergence curves
Conventional
Extended

## Slide 55: Optimal extended perturbation -
Zero time-lag section of

## Slide 56: Optimal extended perturbation -
CIG of

## Slide 57: Optimal extended perturbation -
CIG of
EXTENDED
MODELING

## Slide 58: Data-fitting term - Summary
Correcting term can be computed for any
: extended Born modeling operator
: optimal extended perturbation perturbation

## Slide 59: Data-fitting term - Summary
“As small as we want”

## Slide 60: Data-fitting term - Summary
Correcting term can be computed for any
: extended Born modeling operator
: optimal extended perturbation

## Slide 61: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
Gradient

## Slide 62: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
Gradient

## Slide 63: Goal of regularization term
Keep this term “small”

## Slide 64: Goal of regularization term
make vanish
keep data-fitting term “small”

## Slide 65: Regularization operator
Modified differential semblance optimization (DSO)
Invertible, linear, diagonal
Enhances non-zero energy of

## Slide 66: Regularization operator – Penalty function

## Slide 67: Regularization operator
Modified differential semblance optimization (DSO)
Invertible, linear, diagonal
Enhances all the energy of

## Slide 68: Regularization term - Summary
Gradually reduces energy of correcting term
Takes advantage of DSO convergence properties (Sava and Biondi, 2004)
Fundamental difference from TFWI (Biondi and Almomin, 2014)
  must vanish completely
  Enhances all energy including the non-extended space
  No physical meaning attached to
: Trade-off parameter between data-fitting and regularization
  Fixed throughout inversion

## Slide 69: Regularization term - Summary
Keep this term “small”
Make vanish

## Slide 70: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
Gradient

## Slide 71: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
  Computation of
  Effect of
Gradient

## Slide 72: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
  Computation of
  Effect of
Gradient

## Slide 73: Variable projection step – Computing
fixed
: computed by minimizing quadratic function

## Slide 74: Variable projection step – Computing
fixed
: computed by minimizing quadratic function

## Slide 75: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
  Computation of
  Effect of
Gradient

## Slide 76: Effect of
3 cases:
FWI data-residuals

## Slide 77: Effect of on data-fitting

## Slide 78: Effect of on data-fitting

## Slide 79: Effect of on data-fitting

## Slide 80: Effect of on (CIG at )

## Slide 81: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
  Computation of
  Effect of
Gradient computation

## Slide 82: Dissection of FWIME
Objective function
Data-fitting term
Regularization term
Variable projection step
  Computation of
  Effect of
Gradient computation

## Slide 83: Gradient computation
GRADIENT FROM CORRECTING TERM
SIMILAR TO
CONVENTIONAL FWI
GRADIENT

## Slide 84: Gradient computation
TOMOGRAPHIC
BORN

## Slide 85: Gradient computation
FWIME data residual

## Slide 86: Numerical example – Velocity model
Interface
True velocity model
1D velocity profiles
Interface

## Slide 87: FWI first search direction
True interface position

## Slide 88: FWIME first search direction – Born component
True interface position

## Slide 89: FWIME first search direction – Tomo component

## Slide 90: FWIME first search direction (Born + tomo)

## Slide 91: FWIME first search direction - Spline grid

## Slide 92: FWIME first search direction after spline interpolation

## Slide 93: Ideal search direction

## Slide 94: FWIME first search direction - Summary
Born component
Tomographic component
Total search direction (Born + tomographic)
Total search direction with spline

## Slide 95: Inversion of reflection data: The Marmousi model

## Slide 96: Velocity models – 2D panels

## Slide 97: Velocity models – 1D profiles ()

## Slide 98: Inverted seismic data
Data-space multi-scale approach
  Energy between 4-15 Hz
  5 frequency-bands
Acoustic noise-free data
  500 receivers (20m spacing)
  100 sources (100m spacing)
  10 km-offset maximum
  8s recording
Reflected and refracted energy
FWI

## Slide 99: Conventional FWI – Frequency content

## Slide 100: Inverted seismic data
Data-space multi-scale approach
  Energy between 4-15 Hz
  5 frequency-bands
Acoustic noise-free data
  500 receivers (20m spacing)
  100 sources (100m spacing)
  10 km-offset maximum
  8s recording
Reflected and refracted energy
FWI

## Slide 101: Inverted seismic data
Data-space multi-scale approach
  Energy between 4-15 Hz
  5 frequency-bands
Acoustic noise-free data
  500 receivers (20m spacing)
  100 sources (100m spacing)
  10 km-offset maximum
  8s recording
Reflected and refracted energy
FWI

## Slide 102: Shot gathers inverted with FWI

## Slide 103
Initial model

## Slide 104
Conventional FWI

## Slide 105
True model

## Slide 106: Inverted seismic data
Data-space multi-scale approach
  Energy between 4-15 Hz
  5 frequency-bands
Acoustic noise-free data
  500 receivers (20m spacing)
  100 sources (100m spacing)
  10 km-offset maximum
  8s recording
Reflected and refracted energy
FWI

## Slide 107: Inverted seismic data
FWIME
Data-space multi-scale approach
  Energy between 4-15 Hz
  5 frequency-bands
Acoustic noise-free data
  500 receivers (20m spacing)
  100 sources (100m spacing)
  10 km-offset maximum
  8s recording
Reflected and refracted energy
FWI
Model-space multi-scale approach
  Energy between 4-15 Hz
  4 spline grid dispositions

## Slide 108: Frequency content
FWIME

## Slide 109: Inverted seismic data
FWIME
Data-space multi-scale approach
  Energy between 4-15 Hz
  5 frequency-bands
Acoustic noise-free data
  500 receivers (20m spacing)
  100 sources (100m spacing)
  10 km-offset maximum
  8s recording
Reflected and refracted energy
FWI
Model-space multi-scale approach
  Energy between 4-15 Hz
  4 spline grid dispositions
Acoustic noise-free data
  500 receivers (20m spacing)
  100 sources (100m spacing)
  6 km-offset maximum
  5s recording
Reflected energy only

## Slide 110: Shot gathers inverted with FWIME

## Slide 111: First iteration of FWIME -

## Slide 112: First iteration of FWIME -
Compute FWI data residual
Compute
Compute gradient

## Slide 113: Initial data

## Slide 114: First iteration of FWIME -
Compute FWI data residual
Compute gradient

## Slide 115: First iteration of FWIME -
Compute FWI data residual
Compute
Compute gradient

## Slide 116: A close look at

## Slide 117: A close look at

## Slide 118: A close look at

## Slide 119: A close look at

## Slide 120: A close look at

## Slide 121: A close look at

## Slide 122: First iteration of FWIME -
Compute FWI data residual
Compute
Compute gradient

## Slide 123: First search direction
FWIME

## Slide 124: Ideal search direction
IDEAL

## Slide 125: First search direction after spline interpolation
FWIME + SPLINE

## Slide 126: Ideal search direction after spline interpolation
IDEAL + SPLINE

## Slide 127
Initial model

## Slide 128
FWIME – First spline grid

## Slide 129
FWIME – Last inverted model

## Slide 130
True model

## Slide 131
FWIME + FWI
FWIME + FWI

## Slide 132
True model

## Slide 133
Conventional FWI

## Slide 134: as a QC tool
Evolution of for first spline disposition
Evolution of for last spline disposition

## Slide 135: as a QC tool

## Slide 136: as a QC tool

## Slide 137: as a QC tool

## Slide 138: as a QC tool

## Slide 139: as a QC tool – Initial

## Slide 140: as a QC tool – After spline #1

## Slide 141: as a QC tool
Evolution of for first spline disposition
Evolution of for last spline disposition

## Slide 142: as a QC tool – Initial spline #4

## Slide 143: as a QC tool – Final spline #4

## Slide 144: as a QC tool – Initial spline #4

## Slide 145: as a QC tool – Final spline #4

## Slide 146: Evolution of throughout FWIME
Initial
After spline #1
Initial spline #4
Final

## Slide 147: Making it feasible in 3D: Accelerating the variable projection step

## Slide 148: FWIME main challenge - Variable projection step
Computed iteratively until convergence
Must be recomputed for every tested
Accounts for 99% of total computational cost of FWIME!
Notes: Mention that you need to reach vp convergence for optimal gradient

## Slide 149: How many iterations do we need?

## Slide 150: Preconditioning the iterative process
The optimal perturbation is given by:

## Slide 151: Preconditioning the iterative process
The optimal perturbation is given by:

## Slide 152: Preconditioning the iterative process
The optimal perturbation is given by:
Hessian of the linear problem

## Slide 153: Preconditioning the iterative process
The optimal perturbation is given by:
Hessian of the linear problem
FWI residuals

## Slide 154: Preconditioning the iterative process
The optimal perturbation is given by:

## Slide 155: Preconditioning the iterative process
The optimal perturbation is given by:
Hou and Symes (2017) derived an approximate pseudo inverse:

## Slide 156: Preconditioning the iterative process
The optimal perturbation is given by:
Hou and Symes (2017) derived an approximate pseudo inverse:

## Slide 157: Preconditioning the iterative process
The optimal perturbation is given by:
Hou and Symes (2017) derived an approximate pseudo inverse:

## Slide 158: Preconditioning the iterative process
The optimal perturbation is given by:
Hou and Symes (2017) derived an approximate pseudo inverse:

## Slide 159
With one migration process we match more than 80% of the data!

## Slide 161: Zero time-lag cross-section
Linear CG – iteration #100

## Slide 162: Zero time-lag cross-section

## Slide 163: Future steps
Implement weighted CG algorithm (Hou and Symes, 2015)
Find pseudo inverse for regularized problem
Adapt to different kind of extensions

## Slide 164: Conclusions and opportunities

## Slide 165: Conclusions
Successfully applied FWIME
  Model-space multi-scale approach
  Reflection data
  Short offsets
  Lack of low frequencies
  Inaccurate starting model
provides QC tool for inversion process
FWIME requires minimum user input
  Spline refinement rate
  -value

## Slide 166: Next steps and opportunities
Conduct FWIME workflow until full convergence
Accelerate variable project step (3D applications)
Assess robustness with elastic data and noise
Automatize
  Selection of -parameter
  Spline grid refinement rate
Suggest models (2D or 3D) to benchmark FWIME

## Slide 167
In reality the subsurface is certainly elastic
Vp
Vs
Density

## Slide 168
In reality the subsurface is certainly elastic
Vp
Vs
Density

## Slide 169
In reality the subsurface is certainly elastic
Vp
Vs
Density
Redatuming using linearized extended waveform inversion (SEP 172)
True amplitude migration (tomorrow @8:00am)

## Slide 170
Vp
However, we need an accurate acoustic velocity model!
?

## Slide 171
Reservoir elastic properties
Elastic data as if it was acquired on top of the target area
An ideal workflow
Data pre-processing
Acoustic model building FWIME
Redatuming by
Extended Linearized Waveform Inversion
Target-oriented elastic FWI
Accurate overburden velocity model

## Slide 172: Thank you – Questions?

## Slide 173: Acknowledgements
We would like to thank William Symes for useful discussions and guidance

## Slide 174: Auxiliary slides

## Slide 175: Inversion of refracted waves
TRUE
FWI
FWIME + FWI
FWIME

## Slide 176: Inversion of refracted waves - FWIME®
FWIME
FWIME + FWI

## Slide 177: Inversion of refracted waves - FWI
3-5 Hz
3-12 Hz

## Slide 178: Summary – Recap what we are showing in the presentation
We successfully apply FWIME on reflection data and avoid cycle-skipping

## Slide 179
Add a slide at the end to explain how Ettore’s and my projects are linked
We want to create a full solution
Accurate background
  Good images (Earth structure)
  Elastic parameters (reservoir fluid content)

## Slide 180: How to pick g(m)?
We choose to pick g(m)=Bp
Explain that B tilde is the extended demigration operator (its adjoint is well-known: extended RTM)
We claim that we can always find an extended p that matches any data residual (if we set it up as an inverse problem)
Show 2 examples,
  Diving waves
  Complex salt body (power of the extended modeling)
Mention that matching the data residuals is useless by itself
The data-fitting term enables us to maintain control on the level of data matching

## Slide 181: Outline – Junk
Theoretical review
  Objective function – Example on borehole transmission data
  Data-fitting term – Example on Marmousi starting with water velocity
  Regularization term – Show the modified DSO
  Variable projection – Combining everything together
  Gradient computation - Discuss with Ettore how to explain tomo (conceptually)
Step-by-step dissection of FWIME – Example on Mora2.0
  First step of FWIME
  Vp + Pick epsilon
  Compute gradient (+spline)
  Compare for FWI
Inversion of reflection data – Marmoush
  Stuff from paper (CIGs, zero-offset sections)
  Explain that high-resultion data -> higher resolution p -> higher accuracy on moveout info -> better tomo gradient
Making it feasible in 3D – Symes’ preconditioning
  Explain that the vp step accounts for 95% of FWIME cost ($$$)
  Show example that illustrate the importance of converging for VP (effect on the gradient vs iteration on curve) (we have to do it)
  Solutions: Symes’ preconditioning
    Theory (show the equation of the approximate pseudo-inverse) and explain the cost (very cheap) and the different terms
    Show convergence curves, extended images (zero-offset + cigs + predicted data)
    Explain that we are trying to adapt it to the regularized version
Conclusions and opportunities

## Slide 182: Goal of regularization term
Keep this term “small”
make vanish

## Slide 183: FWIME objective function
: Data correcting term
: Enhances energy of data-correcting term

## Slide 184: FWIME objective function

## Slide 185: FWIME objective function
: Data correcting term
: Enhances energy of data-correcting term