## Slide 1: Time-lapse full waveform inversion (FWI): estimating stress-induced anisotropic parameter changes
Yinbin Ma
05/14/2019
Stanford Exploration Project
Yinbin Ma1,3, Timur Garipov2, Stew Levin1, Biondo Biondi1,3, Hamdi Tchelepi2,3 (Stanford University), and Mark A. Meadows (Chevron ETC)
Geophysics Department
Energy Resource Engineering Department
Institute of Computational and Mathematical Engineering

## Slide 2
Overview
Motivation: why stress-induced anisotropic parameters change
4D VTI model building from coupled flow-geomechanical simulation
Sensitivity analysis of seismic data
Preliminary 4D FWI results

## Slide 3: Genesis (GOM) production wells – Failed in Red
Figure from M. Maharramov, Ph.D. Thesis, SEP-162, 2016
Production related depletion, reservoir compaction, overburden dilation are common interest of seismic imaging, reservoir simulation, and geomechanics

## Slide 4
Seismic modeling & inversion
Geophysics, Stanford
Coupled flow & geomechanics
ERE, Stanford

## Slide 5
long term goal: closed-loop solution for reservoir monitoring
Seismic modeling & inversion
starting seismic model for 4D FWI
Constraints/update on geomechanical model
Coupled flow & geomechanics

## Slide 6: This presentation: feasibility study of geomechanics to seismic
Seismic modeling & inversion
Coupled flow & geomechanics
seismic model for synthetic FWI study
Goal # 1: feasibility to build time-lapse seismic model?
Goal # 2: understand the limitations of the acquisition geometry.
Goal # 3: develop 4D FWI strategies.

## Slide 7
Is there a measurable 4D anisotropic effect from seismic data?
M. Maharramov, Ph.D. Thesis, SEP-162, 2016
Time-lapse velocity change
Our goal is to go beyond isotropic model to make connection between seismic and geomechanics

## Slide 8
Middle panel will be muted at presentation
Maximum offset 4.5 km
Maximum offset 7.2 km
Baseline
Monitor
Common shot gathers after data re-processing

## Slide 9
RTM images
Ma et al., SEP 168, 2017
VTI model is built based on NMO velocity
Not updated with FWI, tomography, etc

## Slide 10: Analysis of depth shifts in migrated images Migrate both baseline and monitor data, with the same VTI model
Anisotropic migration of baseline

## Slide 11: Analysis of depth shifts in migrated images Migrate both baseline and monitor data, with the same VTI model
Anisotropic migration of monitor

## Slide 12: Analysis of depth shifts in migrated images Migrate both baseline and monitor data, with the same VTI model
Anisotropic migration of baseline

## Slide 13: Analysis of depth shifts in migrated images Migrate both baseline and monitor data, with the same VTI model
Anisotropic migration of monitor

## Slide 14: Analysis of depth shifts in migrated images Migrate both baseline and monitor data, with the same VTI model
Near offsets see an area of decreasing velocity, but far offsets do not
We have no clue about time-lapse changes in anisotropic parameters
V-

## Slide 15
Overview
Motivation: why stress-induced anisotropic parameter changes
4D VTI model building from coupled flow-geomechanical simulation
Sensitivity analysis of seismic data
Preliminary 4D FWI results

## Slide 16
VTI model building
Finite element geomechanics model
Finite difference seismic model
Young’s modulus
Geometry challenge (FEM->FDM, scaling, artificial boundary at cell faces)
Physical challenge:
  find equations that convert geomechanical properties to seismic properties
  approximation from isotropic to anisotropic model
Vertical velocity

## Slide 17
VTI model building: geomechanical properties
The geomechanical model is isotropic
Young’s modulus, Poisson’s ratio, and density do not change with time (limited by the simulation)
Young’s modulus
Density
Poisson’s ratio

## Slide 18
VTI model building: geomechanical properties
Significant strain changse at reservoir due to depletion
Negligible volumetric strain changes in the overburden
Vertical strain changes due to overburden dilation
Volumetric strain changes
Vertical strain changes

## Slide 19
VTI model building: baseline models
We can directly build isotropic velocity model from geomechanics
Vp
Vs

## Slide 20
VTI model building: baseline model
Vz is the isotropic Vp
We add artificial anisotropy to baseline model
Our purpose is to study time-lapse FWI, therefore we are safe as long as the baseline model is reasonable
Vz
Epsilon
Delta

## Slide 21
VTI model building: monitor model
We use 3rd order elasticity equations to compute the (orthorhombic) stiffness tensor change as a function of strain.
We scale the strain to remove plastic deformation
The geomechanical simulation is done in an isotropic medium, but we apply the modeled strains to anisotropic tri-axial equations
The resulting monitor stiffness perturbations are orthorhombic in the triaxial stress-state reference frame
The final monitor model is projected to nearest VTI model
Dellinger, J., 2005, Computing the optimal transversely isotropic approximation of a general elastic tensor, GEOPHYSICS, 70 , I1–I10.
Stiffness tensor changes
Strain changes

## Slide 22
VTI model building: monitor model
We use 3rd order elasticity equations to compute the (orthorhombic) stiffness tensor change as a function of strain.
We scale the strain to remove plastic deformation
The geomechanical simulation is done in an isotropic medium, but we apply the modeled strains to anisotropic tri-axial equations
The resulting monitor stiffness perturbations are orthorhombic in the triaxial stress-state reference frame
The final monitor model is projected to nearest VTI model
Dellinger, J., 2005, Computing the optimal transversely isotropic approximation of a general elastic tensor, GEOPHYSICS, 70 , I1–I10.
Stiffness tensor changes
Strain changes
plastic component
elastic component

## Slide 23
Vertical velocity
Epsilon
Delta
Eta
VTI model building: time-lapse change

## Slide 24
Vertical velocity
Epsilon
Delta
Eta
VTI model building: time-lapse change
Goal # 1: feasibility to build time-lapse seismic model? Yes, it is feasible
Goal # 2: understand the limitation of the acquisition geometry.
Goal # 3: develop 4D FWI strategies.

## Slide 25
Overview
Motivation: why stress-induced anisotropic parameter changes
4D VTI model building from coupled flow-geomechanical simulation
Sensitivity analysis of seismic data
Preliminary 4D FWI results

## Slide 26
Anisotropic migration of baseline
Maximum offset = 5km
Experiment 1: can we detect changes from seismic data?
Migrate both baseline and monitor data, with the same VTI model

## Slide 27
Anisotropic migration of monitor
Maximum offset = 5km
Experiment 1: can we detect changes from seismic data?
Migrate both baseline and monitor data, with the same VTI model

## Slide 28
Anisotropic migration of baseline
Maximum offset = 5km
Experiment 1: can we detect changes from seismic data?
Migrate both baseline and monitor data, with the same VTI model

## Slide 29
Anisotropic migration of monitor
Maximum offset = 5km
Experiment 1: can we detect changes from seismic data?
Migrate both baseline and monitor data, with the same VTI model

## Slide 30
Anisotropic migration of baseline
V-
Maximum offset = 5km
Experiment 1: can we detect changes from seismic data?
Migrate both baseline and monitor data, with the same VTI model

## Slide 31
Anisotropic migration of monitor
V-
Maximum offset = 5km
Experiment 1: can we detect changes from seismic data?
Migrate both baseline and monitor data, with the same VTI model

## Slide 32
Anisotropic migration of monitor
V-
We should be able to detect production-induced velocity changes with short-offset (5km) data.
Maximum offset = 5km
Experiment 1: can we detect changes from seismic data?
Migrate both baseline and monitor data, with the same VTI model

## Slide 33
Anisotropic migration of baseline
Maximum offset = 5km
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown

## Slide 34
Anisotropic migration of monitor
Maximum offset = 5km
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown

## Slide 35
Anisotropic migration of monitor
Maximum offset = 5km
4D anisotropic parameters has negligible effect on the curvature of angle gathers with 5km offset
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown

## Slide 36
Anisotropic migration of baseline
Maximum offset limited by the size of the model, ~ 15 km
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown

## Slide 37
Anisotropic migration of monitor
Maximum offset limited by the size of the model, ~ 15 km
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown

## Slide 38
Anisotropic migration of monitor
Maximum offset limited by the size of the model
Production induced changes in anisotropic parameters can be detected if:
Long-offset data
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown

## Slide 39
Anisotropic migration of monitor
Maximum offset limited by the size of the model
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown
Production induced changes in anisotropic parameters can be detected if:
Long-offset data
Data are clean
No significant non-repeatability issues
Careful data processing
Accurate estimation of the velocity model

## Slide 40
Anisotropic migration of monitor
Maximum offset limited by the size of the model
Goal # 1: feasibility to build time-lapse seismic model? Yes, it is feasible!
Goal # 2: understand the limitation of the acquisition geometry. We need long-offset data!
Goal # 3: develop 4D FWI strategies.
Experiment 2: can we detect changes in anisotropic parameters?
Migration baseline and monitor data with correct Vz, Vnmo, and assume changes in eta is unknown

## Slide 41
Overview
Motivation: why stress-induced anisotropic parameter changes
4D VTI model building from coupled flow-geomechanical simulation
Sensitivity analysis of seismic data
Preliminary 4D FWI results

## Slide 42
Baseline VTI model
Vertical velocity
Epsilon
Delta

## Slide 43
Time-lapse changes
True Eta changes

## Slide 44
Time-lapse changes
True Eta changes
Estimated Eta changes
Offsets up to 5 km

## Slide 45
Time-lapse changes
True Eta changes
Estimated Eta changes
Offsets up to 5 km
Estimated Eta changes
Offsets up to 20 km

## Slide 46
Time-lapse changes
True Eta changes
Estimated Eta changes
Offsets up to 5 km
Estimated Eta changes
Offset up to 20 km
Goal # 1: feasibility to build time-lapse seismic model? Yes, it is feasible!
Goal # 2: understand the limitation of the acquisition geometry. We need long offset data!
Goal # 3: develop 4D FWI strategies. In progress.

## Slide 47
Next: how can we improve 4D VTI FWI results?
We have no control over the data acquisition, data processing
Non-physical constraint (no extra info added)
  Minimum-norm
  Total-variation regularization
Physical/geological constraint (extra info added)
  Image alignment between baseline image and monitor image
  Constraint by elasticity equations

## Slide 48
Preliminary results
Eta
True model
Eta
Correct sign at shallow area
wrong sign at shallow area
Inversion without reg

## Slide 49
Preliminary results
Eta
Eta
True model
Eta
Correct sign at shallow area
wrong sign at shallow area
Inversion without reg
Minimum norm reg

## Slide 50
Preliminary results
Eta
Eta
True model
Eta
Correct sign in shallow area
wrong sign at shallow area
Inversion without reg
Minimum norm reg
Eta
Total variation reg

## Slide 51: This presentation: feasibility study of geomechanics to seismic
Seismic modeling & inversion
Coupled flow & geomechanics
seismic model for synthetic FWI study
Goal # 1: feasibility to build time-lapse seismic model? Yes, it is feasible!
Goal # 2: understand the limitation of the acquisition geometry. We need long offset data!
Goal # 3: develop 4D FWI strategies. In progress

## Slide 52
Summary of workflow and road ahead
3rd order elasticity
Seismic data
Coupled flow & geomechanics
Time-lapse change of stiffness tensor
modeling
Time-lapse change of seismic properties
Inversion (FWI, etc)
Estimated time-lapse change of stiffness tensor
Estimated time-lapse change of seismic properties
Non-deterministic
Estimated strain
Update geomechanical model
(beyond my work)
We are here==>
Starting point
<== My target

## Slide 53
We would like to thank Chevron, ExxonMobil and BHP for sharing the Genesis dataset
SUPRI-B for providing ADGPRS simulation package
Mark A. Meadows (Chevron) and Timur Garipov (previously Stanford) for their help in this project

## Slide 54
3rd order elasticity
Seismic data
Coupled flow & geomechanics
Time-lapse change of stiffness tensor
modeling
Time-lapse changes of seismic properties
Estimated time-lapse changes of stiffness tensor
Estimated time-lapse changes of seismic properties
Non-deterministic
Estimated strain
Thank you and questions?
We are here==>
Inversion (FWI, etc)
Update geomechanical model
(beyond my work)
<== My target
Starting point

## Slide 55
END OF PRESENTATION

## Slide 56
Backup slides #1: 4D FWI strategies

## Slide 57
FWI on simple synthetic model: baseline model
Vertical velocity
Epsilon
Delta

## Slide 58
Backup slides #2: image alignment

## Slide 59
Physical constraints
Misalignment mostly due to change in Vz
We may use image alignment as regularization to estimate change in Vz