## Slide 1: Using rock physics to improve Qp quantification in seismic data
Yi Shen， Jack Dvorkin
SEP 158, Page 221-234
Stanford Exploration Project

## Slide 2: Outline
Motivation
Theory
  Modeling seismic attenuation
  Modeling velocity
  Linking seismic attenuation and velocity analytically
Validating the closed-form solution using well data
Seismic application: improved Qp quantification in seismic data

## Slide 3: Motivation
Gas pockets or clouds
  are notoriously challenging problems for reservoir identification and interpretation
  have low Qp and low Vp
(Zhou, 2011)

## Slide 4: Motivation
A quantification of the relation between Vp and Qp
  Has been barely studied
  Brings additional information for seismic inversion
True Q
Inverted Q without additional information
Inverted Q with
additional information

## Slide 5: What causes attenuation?
Patchy distribution
Uniform distribution
Water
Gas
Notes: This talk, focused on patchy distribution;

## Slide 6: What causes attenuation?
The oscillatory liquid cross-flow between fully-liquid-saturated patches and the surrounding rock with partial-gas-saturated patches causes attenuation.
Notes: For the illustration: water-gas system
Fluid has viscosity; friction causes attenuation
Atteunation is especatially strong in pathey with partial satuation
Different modulus, pore pressure are different
Wave-induced variation of pore pressure results in the fluid moving in and out of the gas-saturated pore space
Cross-flow causes strong attenuation

## Slide 7: High frequency
Unrelaxed: M∞
Notes: For the illustration: water-gas system
Fluid has viscosity; friction causes attenuation
Atteunation is especatially strong in pathey with partial satuation
Different modulus, pore pressure are different
Wave-induced variation of pore pressure results in the fluid moving in and out of the gas-saturated pore space
Cross-flow causes strong attenuation
Average modulus

## Slide 8: Low frequency
Relaxed: M0
Notes: Porosity: how much the rock is open space

## Slide 9: How to quantify attenuation?
Standard linear solid model relates 1/Qp to the compressional moduli as a function of frequency.
We use the upper bound of 1/Q to describe attenuation, without addressing frequency dependence.
Notes: Don’t expect Q varies with frequency

## Slide 10: How to quantify velocity?
The compressional velocity of rock

## Slide 11: How to relate velocity to Q?
The compressional velocity of rock
The compressional Qp of rock

## Slide 12: How to relate velocity to Q?
MS, ϕ, MDry, KG, KW, Sw, ρ
Vp
Qp
MS: compressional modulus of the mineral phase
ϕ: total porosity
MDry: compressional modulus of the dry frame of the rock
KG and KW: modulus of gas and water, respectively
Sw: water saturation
ρ: bulk density
Notes: For example, phi, merge equation, eliminate phi to link them
We can not take care 7 with 2 equation
we only linked Vp with Qp using the rock properties which, when modified, generate a significant change in these two properties and therefore in their relation.
We assigned a spatially constant value to the rest of the rock parameters.
What we did to find the sensitive

## Slide 13: How to relate velocity to Q?
MS, ϕ, MDry, KG, KW, Sw, ρ
Vp
Qp
MS: compressional modulus of the mineral phase
ϕ: total porosity
MDry: compressional modulus of the dry frame of the rock
KG and KW: modulus of gas and water, respectively
Sw: water saturation
ρ: bulk density
Notes: For example, phi, merge equation, eliminate phi to link them
We can not take care 7 with 2 equation
we only linked Vp with Qp using the rock properties which, when modified, generate a significant change in these two properties and therefore in their relation.
We assigned a spatially constant value to the rest of the rock parameters.
What we did to find the sensitive

## Slide 14: What’s the effects of ϕ

## Slide 15: Link Qp to Vp
The approximate analytical relation

## Slide 16: How the approximation works?
SW = 0.3
Notes: Real worlds, porosity small

## Slide 17: Link Qp to Vp
The approximate analytical relation

## Slide 18: Link Qp to Vp
Notes: Stay validated; sometimes relation fall apart

## Slide 19: How it works on a field gas log

## Slide 20: How it works on a field gas log

## Slide 21: How it works on a field gas log

## Slide 22: Validation
Notes: Real world; dots scattered

## Slide 23: Seismic application
Objectives of seismic inversion for Q
dcal is the calculated data; dobs is the observed data
m is the model, which is Q here; A is the regularization operator
Data
fitting
Model regularization

## Slide 24: Seismic application
Objectives of seismic inversion for Q
dcal is the calculated data; dobs is the observed data
m is the model, which is Q here; A is the regularization operator
Data
fitting
Model regularization

## Slide 25: Velocity and Qp
Velocity
Qp
Li et al. (2015); Want et al. (2013)

## Slide 26: Estimated Q without constraint

## Slide 27: Estimated Q with constraint

## Slide 28: True model

## Slide 29: Before compensation

## Slide 30: After compensation

## Slide 31: Conclusions
We derived an approximate closed-form solution relating Vp to Qp using rock physics modeling.
This solution is validated using field gas well data
We applied our new Qp – Vp to synthetic seismic data
  It produced an improved Q estimated model
  The improved Q model leads to a better seismic migration image

## Slide 32: Acknowledgements
SEP colleagues
SEP sponsors
ThanQ & Q?

## Slide 33: Background review
Modulus:
  Stiffer the rock, the larger the Modulus
  Compressional modulus M= RHOB*Vp*Vp
  Shear modulus G = RHOB*Vs*Vs
  Bulk modulus K = M- 4/3*G
Porosity
  The ratio of pore volume to rock volume
Saturation
  E.g. water saturation: the ratio of water volume to pore volume

## Slide 34: Background review
MS: compressional modulus of the mineral phase
ϕ: total porosity
MDry: compressional modulus of the dry frame of the rock
Notes: Porosity: how much the rock is open space

## Slide 35: Background review
KG: modulus of gas
KW: modulus of water
Sw: water saturation
ρ: bulk density
Notes: Porosity: how much the rock is open space

## Slide 36: Which makes a big change?
SW
MDry
KW
ϕ
MS
MS
ϕ
MDry
KG
KW
Sw
ρ

## Slide 37: Which makes a big change?
ρ
MDry
MS
ϕ
MDry
KG
KW
Sw
ρ
Notes: M dry is the the parameter has significant change to both parameter.
For the rest, some non-sensitive
Some others are sensitive to only

## Slide 38: What is Mdry?

## Slide 39: Which makes a big change?
SW
KW
Ms
ϕ
MS
ϕ
MDry
KG
KW
Sw
ρ

## Slide 40: Which makes a big change?
ρ
ϕ
Ms
MS
ϕ
MDry
KG
KW
Sw
ρ

## Slide 41: Some approximations
The equation of Qp
where 0<SW<1: M0≈M∞; 0=SW or SW<1: M0=M∞
Approximation: define M∞=M0(1+Δ) and use Taylor expansion to reduce the high order of Δ

## Slide 42: Porosity and Saturation
Li et al. (2015); Want et al. (2013)
Porosity
Gas saturation

## Slide 43: Find our αDry

## Slide 44: How the approximation works?
α= 0.05;
SW = 0.3

## Slide 45: How to relate velocity to Q?
MS, ϕ, MDry, KG, KW, Sw, ρ
Vp
Qp
MS: compressional modulus of the mineral phase
ϕ: total porosity
MDry: compressional modulus of the dry frame of the rock
KG and KW: modulus of gas and water, respectively
Sw: water saturation
ρ: bulk density
Notes: For example, phi, merge equation, eliminate phi to link them
We can not take care 7 with 2 equation
we only linked Vp with Qp using the rock properties which, when modified, generate a significant change in these two properties and therefore in their relation.
We assigned a spatially constant value to the rest of the rock parameters.
What we did to find the sensitive

## Slide 46: What is Mdry?
MDry is the compressional modulus of the dry frame of the rock
MDry is not a direct measurable parameter from the well log
The previous studies built the rock physics model to compute MDry using other parameter. (Raymer et al., 1980; Dvokin and Nur, 1996, etc.)
Problem: these models have not provided an analytical equation that can be used conveniently to derive Vp vs Qp

## Slide 47: What is Mdry?
Porosity ϕ
MDry
pore
MDry ~ 1/ϕ

## Slide 48: What is Mdry?
Porosity ϕ
ΔMDry
(Ms - MDry)~ ϕ
pore

## Slide 49: What is Mdry?
Notes: Alpha calibrate;
2 in to 1 param

## Slide 50: How to relate velocity to Q?
MS, ϕ, MDry, KG, KW, Sw, ρ
Vp
Qp
MS: compressional modulus of the mineral phase
ϕ: total porosity
MDry: compressional modulus of the dry frame of the rock
KG and KW: modulus of gas and water, respectively
Sw: water saturation
ρ: bulk density
Notes: For example, phi, merge equation, eliminate phi to link them
We can not take care 7 with 2 equation
we only linked Vp with Qp using the rock properties which, when modified, generate a significant change in these two properties and therefore in their relation.
We assigned a spatially constant value to the rest of the rock parameters.
What we did to find the sensitive

## Slide 51: What’s the effects of ϕ
a = 0.05